## Slide 1: Climate Change: Adaptation and Mitigation
Please read the following (available from class website)
  “A Plan to Keep Carbon in Check” by Robert Socolow and Steve Pacala, Scientific American, 2006
  “Can we Bury Global Warming,” by Robert Socolow, Scientific American, 2005
  “Building a Green Economy,” by Paul Krugman, New York Times Magazine, 2010
  Hot Flat, and Crowded, Chapter 2, by Thomas Friedman, 2008

## Slide 2: What we Know for Sure
CO2 molecules absorb & re-emit thermal radiation (Tyndall, 1863)
Doubling the number of CO2 molecules would add 4 W m-2 to the surface 24/7 (Arrhenius, 1896)
If China and India industrialize with coal, CO2 will approach 400% preindustrial by 2100
Additional CO2 will continue adding heat to Earth’s surface for thousands of years

## Slide 3: What We’re Not So Sure About
When and in precisely what ways the climate will change, especially locally
The economic, political, and social consequences of these changes
What to do about all of this

## Slide 4: The Global Carbon Cycle
Humans
Atmosphere
775 + 4/yr
Ocean
38,000
Land
2000
~90
~120
~120
8 GtC/yr
~90
About half the CO2 released by humans is absorbed by oceans and land
“Missing” carbon is hard to find among large natural fluxes

## Slide 5: Where Has All the Carbon Gone?
Into the oceans
  Solubility pump (CO2 very soluble in cold water, but rates are limited by slow physical mixing)
  Biological pump (slow “rain” of organic debris)
Into the land
  CO2 Fertilization (plants eat CO2 … is more better?)
  Nutrient fertilization (N-deposition and fertilizers)
  Land-use change (forest regrowth, fire suppression, woody encroachment … but what about Wal-Marts?)
  Response to changing climate (e.g., Boreal warming)

## Slide 6: Vertical Structure of the Oceans
Warm buoyant “raft” floats at surface
Cold deep water is only “formed” at high latitudes
Very stable, hard to mix, takes ~ 1000 years!
Icy cold, inky black, most of the ocean doesn’t know we’re here yet!
sfc
4 km

## Slide 7: Climate Change Mitigation
Stabilizing CO2 at 450 ppm would be really hard!

## Slide 8: Paths to 450 ppm

## Slide 9: CO2 “Budget” of the Atmosphere
2
2
=
4
billion tons go out
Ocean
Land Biosphere (net)
Fossil Fuel
Burning
+
8
800
billion tons carbon
4
billion
tons go in
ATMOSPHERE
billion tons added every year
Rob Socolow and Steve Pacala http://www.princeton.edu/wedges/ Climate Mitigation Initiative, Princeton University

## Slide 10: How Far Do We Choose to Go?
Billions of tons of carbon
“Doubled” CO2
Today
Pre-Industrial
Glacial
800
1200
600
400
billions of tons carbon
ATMOSPHERE
(
ppm
)
(570)
(380)
(285)
(190)
Past, Present, and Potential Future
Carbon Levels in the Atmosphere

## Slide 11
Billions of Tons Carbon Emitted per Year
Historical
emissions
0
8
16
1950
2000
2050
2100
Historical Emissions
Notes: 11

## Slide 12
1.6
Interim Goal
Billions of Tons Carbon Emitted per Year
Current path = “ramp”
Historical
emissions
Flat path
Stabilization Triangle
0
8
16
1950
2000
2050
2100
The “Stabilization Triangle”
Notes: 12

## Slide 13
1.6
Billions of Tons Carbon Emitted per Year
Current path = “ramp”
Historical
emissions
Flat path
0
8
16
1950
2000
2050
2100
16 GtC/y
Eight “wedges”
Goal: In 50 years, same
global emissions as today
“Stabilization Wedges”
http://www.princeton.edu/wedges/
Notes: 13

## Slide 14: What is a “Wedge”?
A “wedge” is a strategy to reduce carbon emissions that grows in 50 years from zero to 1.0 GtC/yr. The strategy has already been commercialized at scale somewhere.
1 GtC/yr
50 years
Total = 25 Gigatons carbon
  Cumulatively, a wedge redirects the flow of 25 GtC in its first 50 years. This is 2.5 trillion dollars at $100/tC.
A “solution” to the CO2 problem should provide at least one wedge.

## Slide 15: Helpful (?) “Rules of Thumb” for Emissions vs Climate
1 Wedge = 1 GtC/yr in 2050 = 50 fewer GtC by 2100 = 100 ppm less atmospheric CO2
Average warming ~ 3 C per doubling of CO2 (note logarithmic scale!)
Wedges help logarithmically … last wedge helps a lot more than first wedge!
Business as usual CO2 ~ 1000 ppm by 2100 ~ 4x preindustrial ~ 6 C warming ~ 10 F
Central North America gets ~ 1.5x - 2x global average warming (on land, NH, some snow)

## Slide 16: Bottom Line: Wedges and Warming
Average Warming (in C) = 3 * log2(CO2/280)
= 3 * log10(CO2/280) / log10(2)
Each wedge ~ 100 ppm less atmospheric CO2
Do the math …
1st wedge reduces warming by ~ 0.46 C
2nd wedge reduces warming by another ~ 0.51 C
3rd wedge reduces warming another 0.58 C
4th wedge reduces warming by another 0.67 C
5th wedge reduces warming by another 0.79 C

## Slide 17
Energy Efficiency &
Conservation (4)
CO2 Capture
& Storage (3)
Stabilization
Triangle
Renewable Fuels
& Electricity (4)
Forest and Soil Storage (2)
Fuel Switching
(1)
Nuclear Fission (1)
2007
2057
8 GtC/y
16 GtC/y
Triangle
Stabilization
Fifteen Wedges in 4 Categories
http://www.princeton.edu/wedges/
Notes: 17

## Slide 18
Double the fuel efficiency of the world’s cars or halve miles traveled
Produce today’s electric capacity with double today’s efficiency
Use best efficiency practices in all residential and commercial buildings
Replacing all the world’s incandescent bulbs with CFL’s would provide 1/4 of one wedge
Efficiency
There are about 600 million cars today, with 2 billion projected for 2055
Average coal plant efficiency is 32% today
E, T, H / $
Photos courtesy of Ford Motor Co., DOE, EPA
Sector s affected:
E = Electricity, T =Transport, H = Heat
Cost based on scale of $ to $$$
Notes: “E,T, H” = can be applied to electric, transport, or heating sectors, $=rough indication of cost (on a scale of $ to $$$)

## Slide 19
Substitute 1400 natural gas electric plants for an equal number of coal-fired facilities
A wedge requires an amount of natural gas equal to that used for all purposes today
Fuel Switching
Photo by J.C. Willett (U.S. Geological Survey).
E, H / $
Notes: “E,H” = can be applied to electric or heating sectors, $=rough indication of cost (on a scale of $ to $$$)
Effort needed for 1 wedge:
Build 1400 GW of capacity powered by natural gas instead of coal (60% of current fossil fuel electric capacity)
Requires an amount of natural gas equal to that used for all purposes today
So a slice is 50 LNG tanker discharges/day by 2054 @200,000 m3/tanker, or
one new “Alaska” pipeline/year @ 4 Bscfd.
Detailed Description: NATURAL GAS TURBINES ARE BEING DEVELOPED TO PRODUCE ELECTRICITY IN A SIMPLE, LOW COST ENVIRONMENTALLY FRIENDLY WAY. DOE'S NATIONAL ENERGY TECHNOLOGY LABORATORY (NETL) INITIATED THE ADVANCED TURBINE SYSTEMS (ATS) PROGRAM AND HAS PARTNERED WITH INDUSTRY TO PRODUCE A NEW GENERATION OF HIGH EFFICIENCY GAS TURBINES FOR CENTRAL STATION ELECTRICITY PRODUCTION, USING CLEAN BURNING NATURAL GAS.
700 1-GW baseload coal plants (5400 TWh/y) emit 1 GtC/y.
Natural gas: 1 GtC/y = 190 Bscfd
Yr 2000 electricity:
Coal : 6000 TWh/y; Natural gas: 2700 TWh/y.

## Slide 20: Natural Gas is Mostly Methane (CH4)
Methane is a much more powerful emitter of heat than CO2
Emits nearly 100x more heat than CO2 at a given temperature
Lasts only about 12 years, then breaks down to CO2 + H2O
H
H
C
H
H
Currently 200 times less CH4 than CO2 in the atmosphere

## Slide 21: Gas Contains More Energy Per Carbon Than Coal
Most of the energy in natural gas is in C-H bonds
Most of the energy in coal is in C-C bonds
Electricity from gas emits only half as much CO2 as from coal!

## Slide 22: Electricity from Gas Instead of Coal Might Help Slow the Growth of CO2
Building 1400 gigawatt electric power stations burning gas instead of coal would reduce CO2 emissions as much as doubling the gas mileage of all the world’s vehicles!

## Slide 23: BUT …
Gas leaks during drilling, fracking, completion, production, transport, refining, or electrical generation put CH4 into the atmosphere
Each molecule of CH4 in the air emits 100x more heat than CO2
Leakage of just 3.4% cancels the climate benefit of gas!

## Slide 24: Current Leakage is Way too High!
EPA estimates that industry-wide leakage rate is 2.4%
but recent data from Utah show leakage rates over 7%
Recent measurements from aircraft over NE Colorado show leakage rates of about 9%
Colm Sweeney, NOAA ESRL

## Slide 25
Implement CCS at
800 GW coal electric plants or
1600 GW natural gas electric plants or
180 coal synfuels plants or
10 times today’s capacity of hydrogen plants
Graphic courtesy of Alberta Geological Survey
Carbon Capture & Storage
There are currently three storage projects that each inject 1 million tons of CO2 per year – by 2055 need 3500.
E, T, H / $$
Notes: “E,T, H” = can be applied to electric, transport, or heating sectors, $=rough indication of cost (on a scale of $ to $$$)

## Slide 26
Triple the world’s nuclear electricity capacity by 2055
Nuclear Electricity
Graphic courtesy of NRC
The rate of installation required for a wedge from electricity is equal to the global rate of nuclear expansion from 1975-1990.
E/ $$
Notes: “E” = can be applied to electric sector, $$=rough indication of cost (on a scale of $ to $$$)
Plutonium (Pu) production by 2054, if fuel cycles are unchanged: 4000 t Pu (and another 4000 t Pu if current capacity is continued).
Compare with ~ 1000 t Pu in all current spent fuel, ~ 100 t Pu in all U.S. weapons.
5 kg ~ Pu critical mass.

## Slide 27
Wind Electricity
Install 1 million 2 MW windmills to replace coal-based electricity,
OR
Use 2 million windmills to produce hydrogen fuel
Photo courtesy of DOE
A wedge worth of wind electricity will require increasing current capacity by a factor of 30
E, T, H / $-$$
Notes: “E,T, H” = can be applied to electric, transport, or heating sectors, $-$$=rough indication of cost (on a scale of $ to $$$)

## Slide 28
Solar Electricity
Photos courtesy of DOE Photovoltaics Program
Install 20,000 square kilometers for dedicated use by 2054
A wedge of solar electricity would mean increasing current capacity 700 times
E / $$$
Notes: “E” = can be applied to electric sector, $$$=rough indication of cost (on a scale of $ to $$$)

## Slide 29
Using current practices, one wedge requires planting an area the size of India with biofuels crops
Biofuels
Photo courtesy of NREL
Scale up current global ethanol production by 30 times
T, H / $$
Notes: “T, H” = can be applied to transport or heating sectors, $$=rough indication of cost (on a scale of $ to $$$)

## Slide 30
Conservation tillage is currently practiced on less than 10% of global cropland
Natural Sinks
Photos courtesy of NREL, SUNY Stonybrook, United Nations FAO
Eliminate tropical deforestation
OR
Plant new forests over an area the size of the USA
OR
Use conservation tillage on all cropland
B / $
Notes: “B” = biostorage sector, $=rough indication of cost (on a scale of $ to $$$)

## Slide 31
Wedges Summary
For stabilization of emissions (not CO2) pick any 8 of these 15

## Slide 32: Mitigation Costs and Savings
Emissions reduction in 2030 (tons of CO2e)
Cost per ton of CO2e
Meets stabilization at 450 ppm trajectory
Savings from efficiency largely offset new costs
Efficency (cost < $0)
Alternative technologies (cost > $0)
McKinsey & Company report, 'Pathways to a low-carbon economy - Version 2 of the Global Greenhouse Gas Abatement Cost Curve.'

## Slide 33: Free Market Solutions
A new industrial revolution won’t happen because people want to “do the right thing”
The government can’t just pass a law and create a new global energy economy, any more than they could 200 years ago
If low-carbon-footprint goods and services cost less than “dirtier” ones, people will buy them

## Slide 34: A Policy Spectrum
direct subsidy
“cap and trade”
“tax and rebate”
“command and control”
“market capitalism”

## Slide 35: Imagine it’s 1800, and you’re in charge …
Somebody presents you with a grand idea for transforming the world economy:
  Dig 8 billion tons of carbon out of the ground every year
  Build a system of pipelines, supertankers, railroads, highways, and trucks to deliver it to every street corner on the planet
  Build millions of cars every year, and millions of miles of roads to drive them on
  Generate and pipe enough electricity to every house to power lights & stereos & plasma TVs
… “and here’s the itemized bill …”

## Slide 36: Thinking about Co$t$
Our global society built that very system
We didn’t all go broke building it …
We got rich beyond the avarice of kings!
Now we get to do it again!
How?

## Slide 37: Choose Your Future
Many academics believe:
  “Modern economy is possible only through the subsidy of cheap fossil energy. When we stop burning coal we’ll freeze in the dark!”
I prefer:
  “Modern wealth results from ingenuity and hard work. Before we run out of oil, we’ll invent better technologies for the 21st Century.
  The future is bright.”